Building an Enterprise Network
Part 6: EtherChannel
L2 and L3

Topology from Previous Lab
Begin by using the topology you completed in the previous lab. We currently have configured VLANs,
trunking, routed ports and routing in our switch block, so we have complete reachability between all
device.

EtherChannel
EtherChannel is a port link aggregation technology or protocol developed by Cisco, which allows the
bundling of several physical Ethernet links to form a single logical link between two networking
devices. This aggregation enhances the bandwidth by combining multiple links' capacities and
provides redundancy for higher network resilience. EtherChannel can operate at both Layer 2 and
Layer 3 of the OSI model, enabling flexibility in network design and implementation.
Layer 3 EtherChannel: At Layer 3, EtherChannel aggregates multiple links into a single logical
connection that can route IP packets. This is used between routing devices or between routers and
switches that support Layer 3 operations. Layer 3 EtherChannel enables the aggregation of
bandwidth and redundancy for routed links, enhancing the performance and reliability of inter-VLAN
routing and core network connectivity.
Link Aggregation Control Protocol (LACP): LACP is part of an IEEE standard (802.3ad) that
provides a method for automatically creating EtherChannels by dynamically negotiating with
connected devices.
Port Aggregation Protocol (PAgP): PAgP is a Cisco proprietary protocol similar to LACP, designed
to automatically negotiate the formation of EtherChannel links.
LACP and PAgP facilitate the detection and configuration of links that are capable of aggregation and
ensures that only compatible and properly configured links are aggregated. These protocols are highly
recommended for its ability to dynamically manage link aggregation, thereby reducing the likelihood of
configuration errors and improving network resilience. This facilitates the automatic determination of
which links can be combined based on their configurations and ensures consistent configurations on
both ends of the EtherChannel. While PAgP offers benefits similar to LACP, its use is limited to Cisco
devices.
Static Persistence (Manual Configuration): EtherChannel can also be configured statically, without
using LACP or PAgP for negotiation. This method requires manual configuration of both ends of the
EtherChannel to aggregate the links. While this approach offers simplicity and control, it lacks the
dynamic negotiation and configuration verification features of LACP and PAgP, potentially increasing
the risk of misconfiguration and operational issues.
Note: In this lab we will be configuring Layer 2 and Layer 3 EtherChannel using LACP.

Layer 2 EtherChannel - LACP
At Layer 2, EtherChannel combines multiple Ethernet links into a single logical link that operates
between two switches or between a switch and a server. This configuration is typically used in
scenarios where bandwidth aggregation and link redundancy are critical for the operation of access or
aggregation layer switches within a data center or campus network.
Layer 2 EtherChannel between two switches allows STP to treat the combined physical links (known
as a port channel) as a single logical link. This means all the switchports that are part of the Layer 2
EthernChannel are in the forwarding state.

Configure EtherChannel Using LACP
Starting with the access switches in column 1, configure these commands on each of the two
switches that you want to configure with EtherChannel. This will ensure that both sides of the
channel are configured to negotiate the EtherChannel properly and that load balancing is handled in
the desired way. Remember, it's essential that both ends of the EtherChannel are configured
consistently.

To remove the configuration switchport access vlan 255 from the interface and ensure it functions as a trunk port instead of an access port, you can use the following command:

perl
Copy code
no switchport access vlan 255
This command removes the VLAN assignment from the interface, effectively reverting it to a trunk port.

Explanation:

switchport access vlan 255: This command configures the interface as an access port and assigns it to VLAN 255. Access ports are used to connect end devices like computers or printers, and they carry traffic for only one VLAN.
no switchport access vlan 255: This command removes the VLAN assignment from the interface, indicating that it should no longer function as an access port. After removing this configuration, the interface will behave as a trunk port, capable of carrying traffic for multiple VLANs.
Functionality wise:

With switchport access vlan 255, the interface would function as an access port, allowing traffic only for VLAN 255. This is suitable for connecting an end device that belongs exclusively to VLAN 255.
After removing switchport access vlan 255 and configuring the port as a trunk, the interface will be able to carry traffic for multiple VLANs, making it suitable for connecting to other switches or networking devices where traffic needs to be tagged with VLAN information.

access-1-1(config)#

port-channel load-balance src-dst-ip
inter range fa 0/1-2
shutdown
channel-protocol lacp
channel-group 1 mode active

access-1-2(config)#
conf t
port-channel load-balance src-dst-ip
inter range fa 0/1-2
shutdown
channel-protocol lacp
channel-group 1 mode active

Bring up both interfaces on access-1-1

access-1-1(config)#

inter range fa 0/1-2
no shutdown

Bring up both interfaces on access-1-2

access-1-2(config)#

inter range fa 0/1-2
no shutdown

Repeat the EtherChannel Configuration on the other Access Layer Switches

The Packet Tracer bug above is why we waited before configuring LACP on the other access layer
switches.

access-x-y(config)#

port-channel load-balance src-dst-ip
inter range fa 0/1-2
shutdown
channel-protocol lacp
channel-group 1 mode active
exit

! The following port-channel1 command is only required for Packet Tracer

access-x-y(config)#

conf t
interface port-channel1
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
exit

Add a Second Routed Port between Distribution Switches

Add another physical connection between distribution-1 and distribution-2 using the GigabitEthernet
1/0/23 ports.

Configuring Layer 3 EtherChannel using LACP
These are the commands for configuring a Layer 3 EtherChannel on a Layer 3 switch (or router).
Configure distribution-1 switch.

distribution-1(config)#

inter g 1/0/24
no ip address
exit
interface Port-channel2
no switchport
ip address 10.111.1.1 255.255.255.0
no shutdown
exit
interface range gig 1/0/23-24
no switchport
channel-protocol lacp
channel-group 2 mode active
no shutdown
end

Perform similar commands on distribution-2 switch, using its IPv4 address for the port-channel.

distribution-2(config)#

inter g 1/0/24
no ip address
exit
interface Port-channel2
no switchport
ip address 10.111.1.2 255.255.255.0
no shutdown
exit
interface range gig 1/0/23-24
no switchport
channel-protocol lacp
channel-group 2 mode active
no shutdown
end

Verify L3 EtherChannel with ping
The final verification that everything works is using ping to verify our Layer2 and Layer 3
EthernChannels are operating as expected.
From PC with IPv4 address 10.10.1.100, ping 10.30.4.101. This frame/packet will need to be
forwarded across both Layer 2 and Layer 3 EtherChannels.
C:\> ping 10.30.4.101
Pinging 10.30.4.101 with 32 bytes of data:
Request timed out.
Reply from 10.30.4.101: bytes=32 time<1ms TTL=126
Reply from 10.30.4.101: bytes=32 time<1ms TTL=126
Reply from 10.30.4.101: bytes=32 time<1ms TTL=126
Ping statistics for 10.30.4.101:
Packets: Sent = 4, Received = 3, Lost = 1 (25% loss),
Approximate round trip times in milli-seconds:
Minimum = 0ms, Maximum = 0ms, Average = 0ms
C:\>

Final Configurations
Distribution-1
!
interface Port-channel2
no switchport
ip address 10.111.1.1 255.255.255.0

!
interface GigabitEthernet1/0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface GigabitEthernet1/0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
Access-1-1
!

interface Port-channel1
switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp

channel-group 1 mode active
!

interface FastEthernet0/2
switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
Access-2-1
!

interface Port-channel1
switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
interface FastEthernet0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
Access-1-2
!

interface Port-channel1
switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!

interface FastEthernet0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
Access-2-2
!

interface Port-channel1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
interface FastEthernet0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
Distribution-2
!

interface Port-channel2

no switchport
ip address 10.111.1.2 255.255.255.0

!
interface GigabitEthernet1/0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface GigabitEthernet1/0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
Access-1-3
!

interface Port-channel1
switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
interface FastEthernet0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
Access-2-3
!

interface Port-channel1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
interface FastEthernet0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
Access-1-4
!

interface Port-channel1
switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
interface FastEthernet0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
Access-2-4
!

interface Port-channel1
switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate

!
interface FastEthernet0/1

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!
interface FastEthernet0/2

switchport trunk native vlan 254
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport mode trunk
switchport nonegotiate
channel-protocol lacp
channel-group 1 mode active

!