Building an Enterprise Network
Part 7: DHCPv4

Connecting the DHCPv4 Server to the Network

Physically Connect the Server to the Switch
Connect the server to access layer switch in column 4, level 2 using GigabitEthernet 0/1 port on the
switch.
Note: When using the section filter, case matters.
access-2-4#

show running-config | section interface GigabitEthernet0/1

###interface GigabitEthernet0/1
switchport access vlan 255
switchport mode access
shutdown
access-2-4#

Configuring the Switchport Configuration
The switchport is currently in the parking lot VLAN 255 and shutdown. Configure the port for VLAN 40
and enable the port.

Note: Although not necessary, I prefer to explicitly include commands even though they are part of
my default configuration, and remove commands even though IOS will overwrite it.

access-2-4(config)#

interface g 0/1
no switchport access vlan 255
switchport mode access
switchport access vlan 40
no shutdown

Verify IPv4 Address via DHCP on 10.40.0.0/16

On the PCs connected to VLAN 40 and enabled for DHCPv4 (level 2 switches on column 2 and 3) verify
the PCs can now obtain the IPv4 addressing from the DHCPv4 server.
Depending on the client operating system, the PC may need to resend its DHCPv4 discover message.
This can be done on Windows using ipconfig /release and ipconfig /renew. You may receive a DHCP
failed on Packet Tracer due to ARP delays and may need to issue the ipconfig /renew command more
than once.

Cisco Packet Tracer PC Command Line 1.0
C:\> ipconfig
FastEthernet0 Connection:(default port)
Connection-specific DNS Suffix..:
Link-local IPv6 Address.........: FE80::260:70FF:FE6B:E32D
IPv6 Address....................: ::
Autoconfiguration IPv4 Address..: 169.254.227.48
Subnet Mask.....................: 255.255.0.0
Default Gateway.................: ::
0.0.0.0
C:\> ipconfig /release
IP Address......................: 0.0.0.0
Subnet Mask.....................: 0.0.0.0
5
Default Gateway.................: 0.0.0.0
DNS Server......................: 0.0.0.0
C:\> ipconfig /renew
DHCP request failed.
C:\> ipconfig /renew
IP Address......................: 10.40.99.1
Subnet Mask.....................: 255.255.0.0
Default Gateway.................: 10.40.0.1
DNS Server......................: 10.88.88.88
C:\>

DHCPv4 Relay
Verify DHCPv4 Unsuccessful on other Networks/VLANs
If you examine the PCs on other IP networks/VLANs they are still not obtaining their IPv4 addressing
from the DHCPv4 server. This is because their DHCP discover messages, which are Ethernet
broadcasts, are staying within their broadcast domains. The DHCPv4 server is never receiving their
DHCPv4 messages.
For example, the PC a VLAN 30:

The ip helper-address command
The ip helper-address command is used in routers to enable DHCPv4 relay, allowing DHCP broadcast
requests from clients on one network segment to be forwarded to a DHCP server on a different
segment. When a DHCP client sends a broadcast request for an IP address, routers typically do not
forward these broadcasts to other networks.
By configuring an ip helper-address, the router converts the broadcast into a unicast packet and
forwards it to the specified DHCP server's IP address. This mechanism enables devices on subnetted
networks or VLANs to communicate with a central DHCP server, facilitating centralized management
of IP address allocation and reducing the need for multiple DHCP servers across different network
segments.
The ip helper-address command
The ip helper-address is typically configured on the Layer 3 switch or router that acts as the default
gateway for the clients. This setup allows the gateway device to intercept and relay DHCP broadcast
requests from clients to the specified DHCP server, even if it's located on a different network
segment.
The ip helper-address function takes DHCP broadcast packets (255.255.255.255) from clients, which
are meant to be local to the subnet, and converts them into unicast packets. It then forwards these
unicast packets directly to the specified DHCP server's IP address, allowing for cross-network DHCP
service communication.
Configuring ip helper-address on Distribution-2 Switch
The Layer 3 switch Distribution-2 is the default gateway for device on 10.30.0.0/16 (VLAN 30)
network. The SVI, interface VLAN 30, has previously been configured to act as the default gateway for
devices in this network.
The ip helper-address 10.30.0.1 255.255.0.0 command will forward DHCP broadcast packets and
converts the destination IPv4 address from 255.255.255.255 to 10.30.0.1.

distribution-2# show running-config | section interface Vlan30
interface Vlan30
mac-address 000c.8533.1201
ip address 10.30.0.1 255.255.0.0
distribution-2#

distribution-2(config)#

interface vlan 30
ip helper-address 10.40.0.99

Note: Notice that we did not have to use the ip helper-address command for devices on VLAN 40
because they are on the same broadcast domain as the DHCPv4 server.
DHCPv4 Relay IPv4 Addressing Details
Here is a break down the IPv4 addressing process in the DHCP relay scenario step by step:
1. Client to Router:
• A DHCP client on the 10.30.0.0/16 network sends a DHCP Discover message to the
network broadcast address, which is 255.255.255.255.
• The source IPv4 address is 0.0.0.0 (since the client doesn’t have an IPv4 address yet),
and the destination is the broadcast address.
2. Router to DHCP Server:
• The router, configured with ip helper-address 10.40.0.99, receives the broadcast on its
interface with IPv4 address 10.30.0.1.
• The router forwards this packet as a unicast packet with the source IPv4 address
10.30.0.1 (the interface it received the broadcast on) and the destination IPv4 address
10.40.0.99 (the DHCP server).
3. DHCP Server to Router:
• The DHCP server receives the Discover message and responds with a DHCP Offer
message.
• This Offer is sent as a unicast packet with the source IPv4 address 10.40.0.99 and the
destination IPv4 address 10.30.0.1 (back to the router's interface that sent the
Discover message).
4. Router to Client:
• Upon receiving the DHCP Offer, the router broadcasts it to the 10.30.0.0/16 network.
• The source IP address remains 10.40.0.99 (DHCP server's IP), but the router broadcasts
it on the local network, so the packet uses the local network broadcast address (e.g.,
10.30.255.255) as the destination to ensure the client receives it.

Verify DHCPv4 and 10.30.0.0/16 Clients
On the PCs connected to VLAN 30, 10.30.0.0/16 network and enabled for DHCPv4 verify they can now
obtain the IPv4 addressing from the DHCPv4 server.
Depending on the client operating system, the PC may need to resend its DHCPv4 discover message.
This can be done on Windows using ipconfig /release and ipconfig /renew. You may receive a DHCP
failed on Packet Tracer due to ARP delays and may need to issue the ipconfig /renew command more
than once.
A PC on VLAN 30:

C:\> ipconfig
FastEthernet0 Connection:(default port)
Connection-specific DNS Suffix..:
Link-local IPv6 Address.........: FE80::20C:85FF:FE19:8754
IPv6 Address....................: ::
IPv4 Address....................: 10.30.99.1
Subnet Mask.....................: 255.255.0.0
Default Gateway.................: ::
10.30.0.1

Configuring ip helper-address on Distribution-1 Switch
Devices on 10.10.0.0/16 (VLAN 10) and 10.20.0.0/16 (VLAN 20) use distribution-1 layer 3 switch as
their default gateway.
So, we will use a similar ip helper-address command for 10.40.0.99 on distribution-1 switch. We will
configure this command on the interfaces the clients use as the default gateways, the SVIs for VLAN
10 and VLAN 20.

distribution-1(config)#

interface vlan 10
ip helper-address 10.40.0.99

exit
interface vlan 20
ip helper-address 10.40.0.99

Spanning Tree PortFast and BPDU Guard
Reasons for PortFast and DHCP
Using portfast is crucial in DHCP environments because it ensures that the switch port immediately
transitions to the forwarding state, bypassing the usual Spanning Tree Protocol (STP) listening and
learning phases. Without portfast, a device connected to the port might time out in its attempt to
obtain an IP address via DHCP, as the port would not be in the forwarding state yet, delaying the
transmission of DHCP requests and responses. By enabling portfast, we minimize the risk of DHCP
timeouts, allowing devices to receive their IP addressing promptly as the port starts forwarding
packets right away.
BPDU Guard is commonly used in conjunction with spanning-tree portfast to prevent accidental
network disruptions that could occur if a switch is connected to a port configured for end devices like

computers or IP phones. When portfast is enabled, it allows the port to skip the usual STP
deliberation phases and immediately start forwarding packets, which is great for quick network
access but risky if a switch is mistakenly plugged into such a port. This could lead to changes in the
spanning tree topology or even create network loops, potentially causing widespread network
outages. BPDU Guard mitigates this risk by automatically shutting down the port if it receives a BPDU,
indicating that a switch or bridge has been connected, thereby preserving the network's stability and
preventing loop conditions.

Add the PC to the Switch

Add a PC to column 1, level 1 switch. Configure the PC to obtain its addressing using DHCP.

Configure the Switchport without PortFast and Attach the PC

Configure the column 1, level 1 switch as a VLAN 40 access port. Since there is no cable connected (or
if the connected device is powered off), the switch port will not detect a carrier signal and will
therefore be in a "down" state.

access-1-4(config)#

interface fa 0/21
no switchport access vlan 255
switchport mode access
switchport access vlan 40
no shutdown

Now attach the PC to fa 0/21. Notice that the switchport is amber until about 50 seconds later when
Spanning Tree transitions the port to forwarding state (green link light).

As described previously, depending on the client OS, it is possible that the device will never receive
IPv4 addressing information from the DHCPv4 server.
Enable PortFast on this switchport to allow the port to transition immediately to the forwarding
state. Also, enable BPDU Guard to ensure that if a switch is attached to this port, the port will be
disabled. Notice the warning message regarding attaching only a “single host.”

access-1-4(config)#

interface fa 0/21
spanning-tree portfast
spanning-tree bpduguard enable

Next, remove the link and attach the same cable a second time. Notice that the port immediately
transitions to forwarding state (green link light) as soon as the cable is plugged into the switchport.
Cleaning up: You can remove the PC that we just added and put that port back to the parking-lot
VLAN and shutdown.

access-1-4(config)#

interface fa 0/21
no switchport access vlan 40
switchport mode access
switchport access vlan 255
shutdown

Add these commands to all other access layer switches with end devices (PCs) attached, regardless if
they are using DHCPv4 or statically configured IPv4 addresses.
Note: Since all 8 access layer use the same switchports that have IP phones connected, you can use
the interface range command to specific both ports at once.

access-x-y(config)#

inter range fa 0/10, fa 0/20
spanning-tree portfast
spanning-tree bpduguard enable

Switchports with IP Phones

Yes, spanning-tree portfast and spanning-tree bpduguard can be enabled on switchports that have
IP phones connected.
Using spanning-tree portfast on a port connected to an IP phone with a built-in switch is generally
considered safe because the switch in the IP phone is typically a simple Layer 2 device that does not
participate in the Spanning Tree Protocol (STP). These built-in switches are designed to handle direct
traffic between the phone and the connected PC and do not propagate BPDU packets that would
participate in the STP process of the broader network.
As a result, the risk of creating a network loop through this connection is minimal. Additionally,
enabling spanning-tree bpduguard on the port provides an extra layer of protection by ensuring that
the port will be automatically disabled if it ever receives a BPDU, further mitigating the risk of
accidental network topology changes.

access-2-4#

show running-config | section interface GigabitEthernet0/1

Interface GigabitEthernet0/1
switchport access vlan 255
switchport mode access
shutdown
access-2-4#