Basic Access Layer Switch Configuration:

#show interfaces trunk
#show interfaces fa 0/10 switchport
#show vlan brief

Commands for both LEVEL 1 and LEVEL 2 Switches

Switch(config)# hostname access-1-1

“name” the hostname by

#hostname access-1-1 and change accordingly

no ip domain-lookup
enable secret class
line con 0
logging synchronous
exec-timeout 0 0
exit
line vty 0 4
password cisco
login
transport input telnet
exit

Configuring VLANS

Commands for both LEVEL 1 and LEVEL 2 Switches

access-1-1(config)#

vlan 10
name admin
exit
vlan 20
name HR
exit
vlan 30
name Sales
exit
vlan 40
name Engineering
exit
vlan 90
name Voice
exit
vlan 100
name Guest
exit
vlan 180
name Management
vlan 254
name Native
exit
vlan 255
name Parking-Lot
exit

Default Port Configuration
interface range fa0/1-24, g0/1-2:

Commands for both LEVEL 1 and LEVEL 2 Switches
all switches

access-1-1(config)#

interface range fa0/1-24, g0/1-2
switchport mode access
switchport access vlan 255
shutdown
exit

switchport access vlan 255

Configuring Active Access Ports

Commands for LEVEL 1 Switches
! LEVEL 1 PC PORTS

access-1-1(config)#

interface fa0/10
switchport mode access
switchport access vlan 10
no shutdown
exit
interface fa0/20
switchport mode access
switchport access vlan 20
no shutdown
exit

The following commands are for LEVEL 2 switches, which in our scenario have both a PC and an IP Phones
connected.

These commands configure the switch ports to handle both data traffic for a connected PC and voice traffic for
an IP Phone. VLAN 10 and VLAN 20 are used for data traffic from PCs connected to ports fa0/10 and fa0/20,
respectively, while VLAN 90 is designated for voice traffic from IP Phones connected to both ports. QoS
settings are applied to prioritize voice traffic, ensuring clear and uninterrupted voice communication. The no
shutdown command ensures that the ports are enabled and ready for use.
Commands for LEVEL 2 Switches

access-2-1(config)#

interface fa0/10
switchport mode access
switchport access vlan 10
switchport voice vlan 90
mls qos trust cos
no shutdown
exit
interface fa0/20
switchport mode access
switchport access vlan 20
switchport voice vlan 90
mls qos trust cos
no shutdown
exit

access-1-1(config)#

Trunking
A trunk is a network link designed to carry multiple VLANs through a single interface by tagging frames with
VLAN identification. This allows for efficient VLAN distribution across switches and network segments, enabling
devices in different VLANs to communicate through the same physical link while maintaining VLAN separation.

Commands for both LEVEL 1 and LEVEL 2 Switches

access-1-1(config)#

interface range fa0/1-2
no switchport access vlan 255
switchport mode trunk
switchport nonegotiate
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport trunk native vlan 254
no shutdown
exit

copy run start

access-1-1(config)#

End Devices

PC-left
• Interface Fa 0: 10.10.0.100 255.255.255.0
• Global Settings > Default Gateway: 10.10.0.1
• Global Settings > Display Name: 10.10.0.100
PC-left
• Interface Fa 0: 10.10.0.101 255.255.255.0
• Global Settings > Default Gateway: 10.10.0.1
• Global Settings > Display Name: 10.10.0.101
PC-right
• Interface Fa 0: 10.20.0.100 255.255.255.0
• Global Settings > Default Gateway: 10.20.0.1
• Global Settings > Display Name: 10.20.0.100
PC-right
• Interface Fa 0: 10.20.0.101 255.255.255.0
• Global Settings > Default Gateway: 10.20.0.1
• Global Settings > Display Name: 10.20.0.101

Packet Tracer Display Names for Switches
LEVEL 1 AND LEVEL 2 Switches
• Global Settings > Display Name: “Hostname”

Second Pair of Switches - Column 2: Level 1 and Level 2

Do the same for the next pair of Level 1 and Level 2 switches in column 2:
• access-1-2
• access-2-2
Make the necessary changes to hostnames and IPv4 addresses.

COLUMN 3 AND COLUMN 4 – LEVEL 2
! BASIC CONFIG
enable
conf t
no ip domain-lookup

hostname access-2-3
hostname access-2-4

enable secret class
line con 0
logging synchronous
exec-timeout 0 0
exit
line vty 0 4
password cisco
login
transport input telnet
exit

! CREATE VLANS

vlan 10
name admin
exit
vlan 20
name HR
exit
vlan 30
name Sales
exit
vlan 40
name Engineering
exit
vlan 90
name Voice
vlan 100
name Guest
vlan 180
name Management
vlan 254
name Native
vlan 255
name Parking-Lot
exit

! DEFAULT

interface range fa0/1-24, g0/1-2
switchport mode access
switchport access vlan 255
shutdown
exit

! LEVEL 2 PC PORTS

interface fa0/10
switchport mode access
switchport access vlan 30
switchport voice vlan 90
mls qos trust cos
no shutdown
exit
interface fa0/20

switchport mode access
switchport access vlan 40
switchport voice vlan 90
mls qos trust cos
no shutdown
exit

! TRUNK

interface range fa0/1-2
no switchport access vlan 255
switchport mode trunk
switchport nonegotiate
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport trunk native vlan 254
no shutdown
exit
end

copy run start