Building an Enterprise Network
Part 2: Switch Block – Distribution Switches

# Adding Distribution, Layer 3 Switches

## Adding the 3560 Switches
dd two 3650 switches, one switch centered switches in columns 1 and 2 and the other switch centered above column 3 and 4 switches:

  - Hostnames: distribution-1 and distribution-2

Between the switch centered switches in columns 1 and 2, add the following cables:
- Ethernet cross-over cable: Access-1-1 G0/1 to Distribution-1 G1/0/1
- Ethernet cross-over cable: Access-1-2 G0/1 to Distribution-1 G1/0/2

Between the switch centered switches in columns 3 and 4, add the following cables:
- Ethernet cross-over cable: Access-1-3 G0/1 to Distribution-2 G1/0/1
- Ethernet cross-over cable: Access-1-3 G0/1 to Distribution-2 G1/0/2

## Distribution-1 Switch

Switch(config)# hostname distribution-1

distribution-1(config)

no ip domain-lookup
enable secret class
line con 0
logging synchronous
exec-timeout 0 0
exit
line vty 0 4
password cisco
login
transport input telnet
exit

## Distribution-2 Switch

Switch(config)# hostname distribution-2

distribution-2(config)

no ip domain-lookup
enable secret class
line con 0
logging synchronous
exec-timeout 0 0
exit
line vty 0 4
password cisco
login
transport input telnet
exit

# Create VLANs

On both distribution switches, create the same VLANs as the access switches.

distribution-1(config)#

vlan 10
name admin
exit
vlan 20
name HR
exit
vlan 30
name Sales
exit
vlan 40
name Engineering
exit
vlan 90
name Voice
vlan 100
name Guest
vlan 180
name Management
vlan 254
name Native
vlan 255
name Parking-Lot
exit

distribution-1(config)#do show vlan brief

# Configure all Ports with Default Configuration
Configure the following default port configurations on both distribution switches.

distribution-1(config)#

interface range g 1/0/1-24, g 1/1/1-4
switchport mode access
switchport access vlan 255
shutdown
exit
# Configure Trunk Ports Between Distribution and Access Switches

## Distribution Switches

Configure the following trunk links on both distribution switches.

distribution-1(config)#

interface range g 1/0/1-2
no switchport access vlan 255
switchport mode trunk
switchport nonegotiate
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport trunk native vlan 254
no shutdown
exit

## Access (Level-1) Switches

On all

access-1-1(config)# and access-1-2 and the rest of the level 1 switches

interface g 0/1
no switchport access vlan 255
switchport mode trunk
switchport nonegotiate
switchport trunk allowed vlan 1,10,20,30,40,90,100,180,254
switchport trunk native vlan 254
no shutdown
exit

Verify connectivity within VLAN

Now that there is a trunk link between column 1 and 2 switches , and column 3 and 4 switches, all devices in the same VLAN should now be able to communicate.
    • 10.10.1.100 can ping 10.10.2.100
    • 10.20.1.100 can ping 10.20.2.100
    • 10.30.3.100 can ping 10.30.4.100
    • 10.40.3.100 can ping 10.40.4.100

## Verify NO connectivity between VLANs (IP networks)

However, because we have not configured any layer 3 routing, there is still no reachability between devices on different IP networks, VLANs.
- 10.10.1.100 canNOT ping 10.20.1.100
- 10.10.1.100 canNOT ping 10.20.2.100
  Configuring the Default Gateways
- These are the default gateways on the PCs.
- • Devices on a VLAN 10 port, 10.10.0.0/16 network have the default gateway 10.10.0.1
- • Devices on a VLAN 20 port, 10.20.0.0/16 network have the default gateway 10.20.0.1
- • Devices on a VLAN 30 port, 10.30.0.0/16 network have the default gateway 10.30.0.1
- • Devices on a VLAN 40 port, 10.40.0.0/16 network have the default gateway 10.40.0.1

## SVIs on Distribution-1

Configure the multi-layer, layer 3, switch distribution-1 with SVIs (switched virtual interfaces) associated with the default gateway of each of its VLANs, IP networks.
- D1: interface vlan 10 – 10.10.0.1/16
- D1: interface vlan 20 – 10.20.0.1/16

distribution-1(config)#

interface vlan 10
ip address 10.10.0.1 255.255.0.0
no shutdown
exit
interface vlan 20
ip address 10.20.0.1 255.255.0.0
no shutdown
exit

## SVIs on Distribution-2

Configure the multi-layer, layer 3, switch distribution-1 with SVIs (switched virtual interfaces) associated with the default gateway of each of its VLANs, IP networks.
- D2: interface vlan 30 – 10.30.0.1/16
- D2: interface vlan 40 – 10.40.0.1/16

distribution-2(config)#

interface vlan 30
ip address 10.30.0.1 255.255.0.0
no shutdown
exit
interface vlan 40
ip address 10.40.0.1 255.255.0.0
no shutdown
exit

# Routing on Distribution Switches

## Verify No Inter-VLAN communications

Verify the IP addressing on 10.10.1.100 PC and that there is connectivity within its own IP network, VLAN, but not to another IP network, VLAN.

## Enable Routing on Layer 3 Distribution Switches

On both distribution switches use the ip routing command to enable IPv4 routing

distribution-1(config)#

ip routing
exit

distribution-2(config)#

ip routing
exit

## Verify Inter-VLAN communications

Now that we have configured enabled routing on bith distribution-1 and distribution-2 switches, verify connectivity between devices on different IP networks, VLANs.

Note: Since we have not yet created and configured connectivity between the distribution switches, there is no reachability between devices in columns 1 and 2 with devices in columns 3 and 4.

end of lab 2

# Inter-Connecting Distribution Switches

There is more than one way configure our network to forward data within the same VLAN (IP network) or between VLANs (different IP networks). Using our campus architecture model and best practices we will add a link between the two distribution switches and treat this link as a separate layer 3 network.

We will begin by connecting an Ethernet cross-over cable on the GigabitEthernet 1/0/24 ports between distribution-1 and distribution-2 switches.

Since these are layer 3 switches, we will make both of these “routed ports” on a separate IPv4 network 10.111.1.0/24.

Note: We could use a /30 or /31 if we need to conserve our IPv4 address space. At the same time, we should be transitioning to IPv6.

## Configure Distribution-1 Routed Port

distribution-1(config)#

interface g 1/0/24
switchport access vlan 255
no switchport
ip address 10.111.1.1 255.255.255.0
no shutdown
exit

## Configure Distribution-2 Routed Port

distribution-2(config)#

interface g 1/0/24
no switchport access vlan 255
no switchport
ip address 10.111.1.2 255.255.255.0
no shutdown
exit

## Verify Routed Port

The routed port can be used by using the show interface <interface> switchport command. The switchport shows as “Disabled”, which indicates that this port is no longer a layer 2 switch port, but is not a layer 3 routed port. “Enabled” would indicate that the port is a layer 2 switch port.

distribution-1# show interface g 1/0/24 switchport

Configure Static Routes to Remote Networks

Distribution-1 switch has IPv4 addresses associated with its SVIs on VLAN 10 (10.10.0.1/16) VLAN 20 (10.20.0.1/16), along with the IPv4 address configured on the routed port g 1/0/24, which makes it directly connected to the following networks:
- 10.10.0.0/16
- 10.20.0.0.16
- 10.111.1.0/24

However, distribution-1 does not know about remote networks via distribution-2. Therefore, we will configure two static routes, one to each of the following remote networks via the next-hop IPv4 address of distribution-2, 10.111.1.2:
- 10.30.0.0/16
- 10.40.0.0.16

distribution-1(config)#

ip route 10.30.0.0 255.255.0.0 10.111.1.2
ip route 10.40.0.0 255.255.0.0 10.111.1.2

Distribution-2 switch has IPv4 addresses associated with its SVIs on VLAN 30 (10.30.0.1/16) VLAN 40 (10.40.0.1/16), along with the IPv4 address configured on the routed port g 1/0/24, which makes it directly connected to the following networks:
- 10.30.0.0/16
- 10.40.0.0.16
- 10.111.1.0/24

However, distribution-2 does not know about remote networks via distribution-1. Therefore, we will configure two static routes, one to each of the following remote networks via the next-hop IPv4 address of distribution-1, 10.111.1.1:
- 10.10.0.0/16
- 10.20.0.0.16

distribution-2(config)#

ip route 10.10.0.0 255.255.0.0 10.111.1.1
ip route 10.20.0.0 255.255.0.0 10.111.1.1

## Distribution Switch Routing Tables

We can verify the directly connected networks and the static routes we just configured by examining the routing tables of each distribution switch.

### Distribution-1 Routing Table

distribution-1# show ip route

## Verify Connectivity Between All IP Networks, VLANS

# Management VLANs

The management VLAN is used to remotely access the layer 2 and layer 3 switches using a separate VLAN 180 associated with 10.180.0.0/16. The management VLAN

Distribution-1 switch and access switches connected to distribution-1 will be on the management VLAN 180 that is associated with the IPv4 network 10.180.1.0/24. The distribution-1 switch will have the IPv4 address 10.180.1.1/24.

Distribution-2 switch and access switches connected to distribution-2 will be on the management VLAN 180 that is associated with the IPv4 network 10.180.2.0/24. The distribution-1 switch will have the IPv4 address 10.180.2.1/24.

Note: Both management VLANs on separate IPv4 networks are both VLAN 180. This is fine because they are separated by the network between distribution-1 and distribution 2 switches. We kept the same VLAN number for simplicity but some network policies will have you use different VLAN numbers.

## Configure Management VLAN on Distribution-1

distribution-1(config)#

interface vlan 180
ip address 10.180.1.1 255.255.255.0
no shutdown
exit

## Configure Management VLAN on Distribution-2

distribution-2(config)#

interface vlan 180
ip address 10.180.2.1 255.255.255.0
no shutdown
exit

## Configure Management VLAN on Access Layer Switches

The default gateway is required on access switches, so these switches, when remotely accessed and acting as a “computer” or “server” can forward packets to a layer 3 device (distribution switch) when telnet/ssh client is on another network.

For access switches, include the distribution layer switch as its default gateway.

access-1-1(config)#

interface vlan 180
ip address 10.180.1.10 255.255.255.0
no shutdown
exit
ip default-gateway 10.180.1.1

The access switches will use the distribution-1 switch IPv4 address as its default gateway.
- Distribution-1: 10.180.1.1/24
- Access-1-1: 10.180.1.10/24, default gateway: 10.180.1.1
- Access-2-1: 10.180.1.20/24, default gateway: 10.180.1.1
- Access-1-2: 10.180.1.30/24, default gateway: 10.180.1.1
- Access-2-2: 10.180.1.40/24, default gateway: 10.180.1.1

The access switches will use the distribution-1 switch IPv4 address as its default gateway.
- Distribution-2: 10.180.2.1/24
- Access-1-3: 10.180.2.10/24, default gateway: 10.180.2.1
- Access-2-3: 10.180.2.20/24, default gateway: 10.180.2.1
- Access-1-4: 10.180.2.30/24, default gateway: 10.180.2.1
- Access-2-4: 10.180.2.40/24, default gateway: 10.180.2.1

For all column 1 and 2 switches, makes distribution-1 the default gateway for the management VLAN.

access-1-1(config-if)#

ip default-gateway 10.180.1.1

For all column 3 and 4 switches, makes distribution-2 the default gateway for the management VLAN.

access-1-3(config-if)#

ip default-gateway 10.180.2.1

distribution-1(config)#

ip route 10.180.2.0 255.255.255.0 10.111.1.2

distribution-2(config)#

ip route 10.180.1.0 255.255.255.0 10.111.1.1