Building an Enterprise Network
Part 3: Routed Ports

Inter-Connecting Distribution Switches

Configure Distribution-1 Routed Port
distribution-1(config)#

interface g 1/0/24
no switchport access vlan 255
no switchport
ip address 10.111.1.1 255.255.255.0
no shutdown
exit

Configure Distribution-2 Routed Port

distribution-2(config)#

interface g 1/0/24
no switchport access vlan 255
no switchport
ip address 10.111.1.2 255.255.255.0
no shutdown
exit

Verify Routed Port

The routed port can be used by using the show interface <interface> switchport command. The
switchport shows as “Disabled”, which indicates that this port is no longer a layer 2 switch port, but is
not a layer 3 routed port. “Enabled” would indicate that the port is a layer 2 switch port.

distribution-1#

show interface g 1/0/24 switchport

Name: Gig1/0/24
Switchport: Disabled
distribution-1#

Configure Static Routes to Remote Networks

Distribution-1 switch has IPv4 addresses associated with its SVIs on VLAN 10 (10.10.0.1/16) VLAN
20 (10.20.0.1/16), along with the IPv4 address configured on the routed port g 1/0/24, which makes it
directly connected to the following networks:
• 10.10.0.0/16
• 10.20.0.0.16
• 10.111.1.0/24

However, distribution-1 does not know about remote networks via distribution-2. Therefore, we will
configure two static routes, one to each of the following remote networks via the next-hop IPv4
address of distribution-2, 10.111.1.2:

• 10.30.0.0/16
• 10.40.0.0.16

distribution-1(config)#

ip route 10.30.0.0 255.255.0.0 10.111.1.2
ip route 10.40.0.0 255.255.0.0 10.111.1.2

Distribution-2 switch has IPv4 addresses associated with its SVIs on VLAN 30 (10.30.0.1/16) VLAN
40 (10.40.0.1/16), along with the IPv4 address configured on the routed port g 1/0/24, which makes it
directly connected to the following networks:
• 10.30.0.0/16
• 10.40.0.0.16
• 10.111.1.0/24
However, distribution-2 does not know about remote networks via distribution-1. Therefore, we will
configure two static routes, one to each of the following remote networks via the next-hop IPv4
address of distribution-1, 10.111.1.1:
• 10.10.0.0/16
• 10.20.0.0.16

distribution-2(config)#

ip route 10.10.0.0 255.255.0.0 10.111.1.1
ip route 10.20.0.0 255.255.0.0 10.111.1.1

Distribution Switch Routing Tables

We can verify the directly connected networks and the static routes we just configured by examining
the routing tables of each distribution switch.